## Slide 1
Smart Desk Lighting System
Embedded AI Final Project · XIAO ESP32S3 Sense
Camera
Capture
▶
MobileNetV2
On-Device
▶
Class
Prediction
▶
PWM
Light Control
computer
Cool Work Light
Cool=250 Warm=0
empty
Lights Off
Cool=0 Warm=0
ipad
Bright Reading
Cool=250 Warm=250
phone
Dim Warm Light
Cool=0 Warm=250
scene → on-device model → class prediction → automatic light mode
Fixed overhead camera captures the desk scene continuously
MobileNetV2 96×96 (0.35 width) runs inference fully on-device
Two PWM LED channels — cool white + warm white — set automatically per class
Notes: SPEAKER NOTES — Slide 1 (0:00 – 0:20) ← quick, ~20 seconds "This is our embedded AI final project — a smart desk lighting system. A camera on the XIAO ESP32S3 Sense watches your desk, runs a lightweight image classification model on-chip, and uses the result to control two LED channels via PWM. Four scenes, four light modes. All on-device — no cloud."

## Slide 2
Model & Data
Model
MobileNetV2 96×96, width 0.35 — lightweight enough to run on ESP32S3
4-class image classification: computer / empty / ipad / phone
Highest-confidence prediction selected each inference cycle
Compiled into Arduino firmware — runs fully on-chip, no cloud
Data
~50 images per class, captured directly from the XIAO camera
Same fixed camera angle used for both training and deployment
Labels match lighting behavior — not object identity
Hard negatives for “empty”: desk with objects visible, but no active user
Notes: SPEAKER NOTES — Slide 2 (0:20 – 0:50) ← ~30 seconds "The model is MobileNetV2 at 96 by 96, width factor 0.35 — chosen because it's small enough to run inference on the ESP32S3 while still being accurate enough for a fixed-view desk scene. We collected about 50 images per class directly from the XIAO camera, at the same angle used for deployment. Labels map to lighting modes, not objects. One thing worth mentioning: the ‘empty’ class includes a desk that still has a keyboard and mouse on it — just no active user. This teaches the model that empty means no one working, not a bare table."

## Slide 3
Design Challenges
✗ Original Plan
Detect hand–object interactions on the desk
Hand on keyboard/mouse → computer mode
Hand on paper/book → reading mode
Problem: hands rest near keyboard even when not typing
→
✓ Final Design
Classify the whole desk scene (no hand detection)
4 scene labels → 4 light modes — direct mapping
More reliable on a fixed camera with a small model
Simpler labels = cleaner data = better consistency
Why Hand Detection Was Too Hard
Low camera resolution and noisy image quality, especially in dim light
Model must be tiny — not enough capacity for fine-grained detection
Hands, keyboard, mouse, and paper visually overlap in the frame
Notes: SPEAKER NOTES — Slide 3 (0:50 – 1:30) ← ~40 seconds "Our original plan was to detect hand-object interactions — hand on keyboard means computer mode, hand on paper means reading mode. But this turned out to be too hard. The camera resolution is limited. The model has to be small. Our dataset is small. And the biggest problem: hands often rest near the keyboard even when you're not typing, so 'hand near keyboard' wasn't a reliable signal. So we simplified: classify the whole scene. No hand tracking, no bounding boxes. Just four scene categories that map directly to lighting modes. This is more robust and still useful."

## Slide 4
Training Results & Demo
93.8%
Accuracy
computer
F1 1.00
empty
F1 1.00
ipad
F1 0.90
phone
F1 0.89
ipad → phone confusion: 18.2%
Both are small devices on the desk — visually similar at 96×96 resolution. All other classes: 100% correct.
ROC AUC
1.00
Precision
0.95
Recall
0.94
F1 (avg)
0.94
What the Demo Shows
Live inference running on XIAO ESP32S3 — no laptop in the loop
Swap desk scenes — watch LED mode switch automatically in real time
Serial output shows the predicted class and confidence each frame
Notes: SPEAKER NOTES — Slide 4 (1:30 – 3:00) (1:30 – 2:00 — Results, ~30 seconds) "The model achieved 93.8% accuracy on the validation set. Computer and empty both hit 100% — those scenes are visually very distinct. The only confusion is ipad getting misclassified as phone 18% of the time. That makes sense — both are small devices laying on the desk, and at 96 by 96 resolution they can look quite similar. Despite that, the weighted F1 is 0.94 and ROC AUC is 1.0." (2:00 – 3:00 — Live demo, full 1 minute — go slowly, let the system speak) "Now the live demo. XIAO on the desk, two LED channels. [clear desk] — empty — lights off. [sit at keyboard] — computer — cool white on, 250 PWM. [place iPad] — ipad — both channels at 250, bright. [put phone down] — phone — cool off, warm on at 250. Everything runs on the chip. Serial output shows the label in real time." ────────────────────────────────────────────────────────────── UPDATED 3-MINUTE VIDEO SCRIPT ────────────────────────────────────────────────────────────── [0:00 - 0:20] Overview (fast) "Smart desk lighting system. Camera on XIAO ESP32S3 Sense watches your desk, classifies the scene into one of four categories, and sets the light automatically. Computer, empty, ipad, phone. All on-device, no cloud." [0:20 - 0:50] Model & Data (steady) "The model is MobileNetV2 at 96 by 96, width 0.35. Small enough to run on the ESP32S3, accurate enough for a fixed-view desk scene. About 50 images per class, captured from the same camera at the same angle. Labels match lighting modes, not object identity." [0:50 - 1:30] Design Challenge (steady) "Originally we wanted to detect hand-object interactions. Hand on keyboard means computer mode, hand on book means reading. But it was too hard: low resolution, small model, small dataset. And hands rest near the keyboard even when you're not typing. So we simplified to full-scene classification. More reliable, cleaner labels." [1:30 - 2:00] Training Results (steady) "93.8% accuracy on the validation set. Computer and empty both scored perfect F1. The only confusion is ipad vs phone, 18% of ipad samples get classified as phone. Both are small devices on the desk, and at 96 by 96 they look similar. Weighted F1 is 0.94, ROC AUC is 1.0." [2:00 - 3:00] Live Demo (slow down, 1 full minute) "Live system. XIAO on the desk, two LED channels. [clear desk] empty - off. [sit at keyboard] computer - cool white on. [place iPad] ipad - both channels bright. [put phone] phone - warm light only. All on-chip. Watch the serial output show the prediction each frame."